## Slide 1: Smoke Detection System
Dhruv Saidava
www.tinkering.in
AP-01-01

## Slide 2: Objective
To detect smoke and prevent fire or suffocation at particular space
Possible scenarios
  Kitchens of Restaurants
  Wood Working Spaces
  Heating Chimneys

## Slide 3: Components Needed
MQ 2 ( Smoke Detection ) Module
Arduino UNO
Micro Controller
Relay
Switch Control
Exhaust Fan
Remove Access Smoke

## Slide 4: Circuit Diagram

## Slide 5: Flow Chart
Fan Off
Detect Smoke Value
Else
More than 120
Fan On
IF

## Slide 6
// the setup routine runs once when you press reset:
void setup() {
// initialize serial communication at 9600 bits per second:
Serial.begin(9600);
pinMode (8, OUTPUT);
}
// the loop routine runs over and over again forever:
void loop() {
// read the input on analog pin 0:
int sensorValue = analogRead(A0);
// print out the value you read:
Serial.println(sensorValue);
delay(1); // delay in between reads for stability

## Slide 7
if (sensorValue <= 120)
{
Serial.println (" Smoke Absent ");
Serial.print (" Value = ");
Serial.println (sensorValue);
digitalWrite (8, LOW);
delay (200);
}
else {
Serial.println (" Smoke Present ");
Serial.print (" Value = ");
Serial.println (sensorValue);
digitalWrite (8, HIGH);
delay (500);
}
}